## Slide 1
STRUCTURAL DYNAMICS RESEARCH
Concrete Bridge Deck and Slab Fatigue under Lane-Free Traffic
Assessment Using a Vehicle–Bridge Interaction Framework
Wang Yanjun
Civil, Environmental and Resources Engineering, Faculty of Engineering, Kyoto University
Research question
How does traffic organization influence concrete deck fatigue performance under the same vehicle fleet?
Computational model
26,520
MITC4 bending/shear plate elements
Coupled steel beams and vertical supports
Approximately 79,600 algebraic coordinates
Linear equivalent model in MATLAB
Study design
22 selected traffic scenarios use the same 240-vehicle fleet, including 20 heavy vehicles.
The comparison varies longitudinal spacing, lateral spread and vehicle ordering, with two-lane and grouped-traffic references.
Compression fatigue
Cumulative damage D = Σ nᵢ/Nᵢ uses the adopted concrete compression S-N relationship. The same eligible observation locations define the comparison.
Maximum damage per 240 vehicles (×10⁻¹⁴)
d = 40 m, traffic increments, K = 17. The range cutoff tests sensitivity to small cycles. Tensile-exceedance locations remain outside the compression assessment.
3 locations / 7 episodes
Grouped traffic exceeds the tensile threshold at three common observation points.
Stress-range coverage
Nominal sections cover all saved observation coordinates.
Recorded stress ranges reach at least 98.53% of the interior field-range upper bound. This measures range-to-bound coverage.
Numerical checks
3,808 independent section-resultant checks and 23,680 cycle/parameter recomputations verify the implementation.
The maximum relative error in recalculating damage is 8.6 × 10⁻¹⁵.
Fatigue interpretation
nᵢ: counted cycles
Nᵢ: cycles from the adopted S-N model
Controlling damage uses S-N continuation beyond two million cycles. Small-cycle treatment affects comparisons. Tensile exceedance remains a separate outcome.
Individual work: model reconstruction, implementation, verification, simulation review and documentation. Professor Kai-Chun Chang supplied the bridge drawings.
Conditional numerical fatigue assessment. Loading, S-N continuation and cycle-cutoff assumptions limit interpretation. No actual service-life prediction.
Chart: 
| Two-lane | Sᵧ 0.05 | Sᵧ 0.10 | Sᵧ 0.15 | Grouped
Full spectrum | 9.5932 | 11.9465 | 10.1912 | 9.3511 | 5.2824
Range ≥0.1 MPa | 0.29783 | 0.94105 | 0.71146 | 0.45909 | 0.95459
Notes: Research sources: nominal reinforced-section concrete surface stresses, common-location compression-fatigue results, tensile-threshold exceedance counts and stress-range upper-bound coverage, October 2026. The displayed five protocols have matched 40 m reference spacing and passage duration. Damage D=sum n_i/N_i uses the adopted compression S-N model, K=17, fd=24/1.3 MPa, permanent stress baseline zero, and traffic-load increments. The full spectrum and 0.1 MPa range cutoff are sensitivity settings. The common compression pool excludes points with tensile exceedance in any case. All controlling damage comes from continuation beyond two million cycles. Grouped traffic has three exceeding locations and seven point episodes; episodes are not vehicles, rainflow cycles or simulated cracks. Minimum stress-range to full-field range-upper-bound coverage is 98.525583843414 percent, not exact full-field history coverage or damage convergence. Professor Kai-Chun Chang provided the drawings and reference materials. No private implementation or source documents are embedded.